## Slide 1: rusEFI knock control proposal

## Slide 2: Important factors for RE knock control
Simple to tune
Computationally efficient, especially in terms of RAM
Tolerant of bad tunes
Tolerant of very different engines
Tolerant of variable fuels
Able to work “good enough” from a base map
Everything here is of maximum importance

## Slide 3: Basics
When knock happens the engine will ring with a bore geometry defined frequency
When this happens we need to retard timing, enrich the mixture or shutdown to protect the engine
Typical retard levels are: 10-20 degrees for low load (30->50 BTDC timing) 5-15 degrees for higher load (15->10 BTDC timing) 1-7 degrees for very high load (10->0 degrees timing) up to 10 for extreme load (0-> -20 BTDC timing)

## Slide 4: Drivability challenges
Knock retard needs to occur quickly and in different amounts at different loads
Knock control needs to be able to cope with a transient
Retard amounts cannot become too large and cause engine to bog down

## Slide 5: Existing infrastructure
Knock sensor electronics work
Noise threshold table already implemented
Knock windowing implemented
Knock frequency select implemented (FFT)
Tests on live engines has shown sensors and FFT system to be able to detect knock

## Slide 6: Proposal for further control logic
Suggest basing knock control around a multiplier and offset strategy
All timing values would be assessed against a baseline timing angle of -20 degrees (20 degrees after TDC)
Upon the first detection of knock RE would take the base table timing value, add 20 to it and multiply this by the “aggression multiplier”.
The resulting value would be removed from the next ignition event
I.e. knock event at 15 degrees, aggression 10% 30 + 20 / 10 = 5 degree ignition retard for the next event
5% to 10% is inline with timing suggestions on page 3
Author suggests doing this math for any given angle or aggression, it seems to still work out with a sensible timing retard step.

## Slide 7: Proposal for further control logic
Whilst knock persists the knock multiplier will wind up and continue to increase in % every time a knock event occurs unless it reaches 100% (-20 degrees spark advance) or the limit configured in an 8x8 table is breached.
At this point there is no more the knock control can do
This determination of degrees of knock to retard by continues until one of two things happens 1 – The knock subsides 2 – We hit the trigger values for either fuel enrichment or shutdown

## Slide 8: Knock subsides
In the event knock subsides and RE can no longer hear knock the ECU would start reapplying timing.
It is suggested that this should happen at half the rate of the retard aggression
If the subsidence of knock caused by a large reduction in load and RPM is it suggested that the knock control reset or reduce to a much lower level. This is due to the driver having likely lifted off the throttle and the in-cylinder conditions having improved to an extent where knock is unlikely

## Slide 9: A trigger threshold is reached
Two trigger thresholds for “fuel enrich” and “shutdown” should be configured
These are trigger points that are triggered by the knock multiplier
If the “fuel enrich” is set to 50% then after 5 knock events at 10% aggression the ECU will enrich the mixture (this will also correspond with the timing having already been reduced significantly)
The “shutdown” is a limit to configure where the ECU will set a low ETB demand or cut the fuel injection and spark to protect the engine. It is an extreme case and would be set high (70%?)

## Slide 10: Cherry on the cake
Incorporating a short term knock memory would allow the ECU to quickly store information on the last known ok timing for a given cell
When knock abates the required knock multiplier would be stored in a small table
Upon the hearing of knock at a given load point the short term table would be checked and the multiplier in the corresponding cell would be applied immediately
This would be a continuous feedback loop of adjusting the timing and preventing knock

## Slide 11: Key benefits
Multiplier is always proportional to the required ignition
This means a single multiplier aggression can be used to configure all the retard steps across the ignition table
Because of this the multiplier calculated at one condition can be applied to varying conditions of a transient and likely still protect against knock, fixed degree steps cannot do this
On an accelerating transient the control will sit on the side of over safe
On a decelerating (closed throttle) transient the system will err towards faster recovery

## Slide 12: Fringe benefits
Multiplier should be very computationally efficient on the STM32
Concepts of knock response aggression, thresholds and multiplier are easy to grasp for users
Minimal parameter to tune for good enough control
Should self adapt to various base maps due to being a multiple of the base map, response is flexible not fixed step

## Slide 13: In summary
One value for knock response aggression %
One value for enrichment trigger %
One value for shutdown trigger %
One 8x8 table for maximum allowed timing retard
Adaptive short term table hidden from user
Log to show current value of each of these to guide users tune - One value for knock frequency (existing) - One table for baseline noise (existing)